## Slide 1: FIXM – GUFI Manfred Beckmann (SOLITEC)
AIXM CCB – 05 December 2016

## Slide 2: Proposed Agenda
Baseline Material
GUFI Format
GUFI Concept and Requirements
GUFI Significant Issues
ICAO FF-ICE Concept
  Use Case Model
  GUFI Provision
  Flight Domain Model
References from FIXM to AIXM
  UML Model
  Sample FIXM message
Lessons Learned?

## Slide 3: Baseline Material
fixm.aero (Flight Information Exchange Model)
  FIXM Core Release v4.0.0 (31-Aug-2016)
  Globally Unique Flight Identifier (GUFI) Format and Content version 2.1 (23-Jun-2014)
  Globally Unique Flight Identifier (GUFI) Requirements version 2.1 (23-June-2014)
  FIXM Implementation Guidance Package version DRAFT (31-Aug-2016)*Updated 31-Oct-2016
aidx.aero (Aviation Information Data Exchange)
ICAO Doc 9965, Manual on Flight and Flow — Information for a Collaborative Environment (FF-ICE)

## Slide 4: GUFI Format
Globally Unique Flight Identifier (GUFI)
  attached to every ATM flight data transaction for a flight
  allow systems to easily and accurately correlate the data
Work carried out previously on the format:
  Natural identifier (information about the flight is encoded in the flight identifier)
    adopted by the Aviation Information Data Exchange (AIDX)
    presently used in a business context by members of the International Air Transport Association (IATA)
  Meta-identifier (information about the GUFI itself is encoded in the flight identifier)
  Uninterpreted identifier (identifier has no semantic content)

## Slide 5: GUFI Concept and Requirements
Two contexts: commercial data and ATM data
  Commercial data: schedules to plan sequences of flights far into the future (up to a year), but also between airline and airport operator to provide status for flights on a given day.
  ATM flight data used to coordinate operation of particular flight between flight operators and ATM service providers.
Only one set of data for a flight, and one GUFI associated with that data set.
Concept of Use
  The first time any ATM data is shared between any two systems for a flight, a GUFI must be assigned to the flight.
  Any system that processes ATM data for a flight must use the GUFI to associate the data in the transaction with its internal representation of the flight’s data.
Interoperability and Transition Requirements defined

## Slide 6: GUFI Significant Issues
Who is responsible for creating GUFIs?
  Flight Operator? ANSP?
How are GUFIs kept unique?  UUID
When does flight data change so much that a new GUFI is needed?
  E.g. flight changes its destination?
What does a transition environment look like?
  E.g. flight transitions GUFI ATM -> legacy ATM -> GUFI ATM
How to make sure only one GUFI is assigned to the same flight?

## Slide 7: ICAO FF-ICE Concept
As of FIXM v4.0.0, requirements come from the FF-ICE/1 implementation manual.
Rather one joint context: Commercial & ATM data

## Slide 8: FF-ICE – Use Case Model

## Slide 9: FF-ICE – GUFI Provision

## Slide 10: FF-ICE – Domain Model

## Slide 11: References from FIXM to AIXM

## Slide 12: References from FIXM to AIXM
<message xsi:type="MessageType"> <flight flightType="S">
<fx:departure> <fx:aerodrome xsi:type="fb:IcaoAerodromeReferenceType" locationIndicator="LOWW"/> <fx:estimatedOffBlockTime timeReference="UTC">2018-01-31T11:20:00.000Z</fx:estimatedOffBlockTime> </fx:departure> <fx:destination> <fx:aerodrome xsi:type="fb:OtherReferenceType" iataDesignator=„BRU"/> </fx:destination> <fx:operator designatorIcao="AUA"> <fb:operatingOrganization name="AUSTRIAN"/> </fx:operator> </flight> </message>

## Slide 13: Lessons Learned?
“To define a unique flight identifier, it is necessary to first define a unique flight.”  Feature identifying properties
Clear responsibility for GUFI creation needed
Still significant issues to be addressed
FIXM references to AIXM via various natural keys