## Slide 1: Overview of the AIXM 5.1 Procedure Model
AIXM Procedure Modelling/Encoding seminar Brussels – 01/02 Sept 2010
Hubert LEPORI Eurocontrol AIM Unit

## Slide 2: Content
Context & History
Overview of the Procedure Model
Procedure Transition, SegmentLeg and SegmentPoint
Approach Conditions (minima…)
Circling Area
MSA
TAA
Miscellaneous
List of open questions

## Slide 3: Procedure = SID, STAR or Approach

## Slide 4: History of the AIXM Procedure Model
AIXM 3.3 / AIXM 4.5:
  Objective: provide an encoding for procedure charts, in support of EAD SDO
  Based on Arinc424-14
  ProcedureLeg was the key of the Procedure model
  Some non-Arinc legs (time-based legs PT/FT) were included

## Slide 5: AIXM 4.5 Procedure Model

## Slide 6: AIXM 4.5 Procedure Model

## Slide 7: History of the Procedure Model
AIXM 5.0/5.1
  Better support the encoding of RNAV procedures published in AIPs
  Support the procedure design process
  Upgrade the model with recent changes in PANS-OPS and Arinc424 (FAS Datablock)

## Slide 8: AIXM 5.1 Procedure Model - Overview
Procedure
The terminal area procedures and related concepts (MSA, TAA...)
Navaids Points
Guidance Service, Point Reference, and Segment Points
Holding
Holding Patterns
Service
For Information services (ATIS) and ATC services
Shared.Surface Assesment

## Slide 9: AIXM 5.1 Procedure Model - Overview
Designator
approachPrefix = Blank
approachType = VOR
multipleIdentification = X
copterTrack = Blanck
circlingIdentification = Blank
courseReversalInstruction = Blank
SID & STAR: designator (+ name?)
Approach: name + 6 first attributes of class InstrumentApproachProcedure

## Slide 10: AIXM 5.1 Procedure Model - Overview
Connection SID/STAR/Appr -> RunwayDirection is realised through class LandingTakeOffAreaCollection
Attribute RNAV is used to identify an RNAV procedure
For an approach, attribute approachType can also carry the value “RNAV”

## Slide 11: AIXM 5.1 Procedure Model - Overview

## Slide 12: Procedure design vs Procedure encoding
The AIXM model defines the class SegmentLeg which represents an elementary portion of a Procedure
A SegmentLeg is associated to a Procedure. A procedure is designed by attaching several SegmentLeg to the procedure
Procedure Design
Procedure Encoding
A Procedure can be divided into a series of Procedure Transitions
More optimised for Procedure Encoding

## Slide 13: Procedure Transition & SegmentLeg
runway
IAF 1
IAF 2
IF
MAP
3 “approach transitions”
1 final approach
1 missed approach
WP 4
FAF
leg 1
leg 1
WPT 1
WP 2
WP 3
leg 2
A Procedure can be divided in a series of Procedure Transitions
A Transition can be represented as a sequence of SegmentLeg
A Transition can be associated with a geographical Curve (for charting and procedure design - not intended for flight)

## Slide 14: Procedure Transition & SegmentLeg
Approach Transition GEBTI
Approach Transition VFA
Final Approach
Missed Approach
SegmentLeg
HoldingPattern

## Slide 15: SegmentLeg
For an approach transition
SegmentLeg contains a set of attributes inspired from the Arinc424 specification
Note: It is not mandatory to use Arinc424 concepts => legPath
SegmentLeg is an abstract class which is specialised:
- 1st specialisation per type of procedure
- 2nd specialisation per type of transition for approach procedures
For a SID
For a STAR
For an Approach
For a final approach
For a missed approach

## Slide 16: SegmentLeg & SegmentPoint
designator = GEBTI
type = ICAO
DesignatedPoint
role = IAF
Waypoint = YES
TerminalSegmentPoint
type = IF
InitialLeg 1
+ startPoint
type = CF
course = 276
courseType = MAG
InitialLeg 2
+ endPoint
Waypoint = NO
Indicator FACF = Yes
Role = IF
TerminalSegmentPoint
role = RAD_DME
PointReference
angle = 96 (276-180)
angleType = MAG
distance = 9 NM
Angle/Distance Indication
Designator = IIF
Navaid

## Slide 17: SegmentLeg - Particular cases
endConditionDesignator = ALTITUDE
lowerLimitAltitude = 2000 ft
MissedApproachLeg
endConditionDesignator = INTERCEPT
MissedApproachLeg
distance = 18 NM
DistanceIndication
designator = TOU
Navaid
+distance

## Slide 18: Approach Conditions
finalApproachPath = STRAIGHT_IN
ApproachCondition
aircraftLandingCategory = C
AircraftCharacteristics
altitude = 218 ft
altitudeCode = OCA
altitudeReference = MSL
height = 200 ft
heightCode = OCH
heightReference = HAT
Minima

## Slide 19: Circling Area

## Slide 20: MSA
safeAreaType = MSA
SafeAltitudeArea
arcDirection = CWA (clockwise Arc)
fromAngle = 284
toAngle = 104
angleDirectionReference = TO
innerDistance = 0 NM
outerDistance = 25 NM
lowerLimit = 1400 ft
lowerLimitReference = MSL
CircleSector 2
arcDirection = CWA (clockwise Arc)
fromAngle = 104
toAngle = 284
angleDirectionReference = TO
innerDistance = 0 NM
outerDistance = 25 NM
lowerLimit = 3000 ft
lowerLimitReference = MSL
CircleSector 1
Designator = VFA
Navaid
+centrePoint

## Slide 21: TAA
designator = LC406
DesignatedPoint
+IF
designator = RIMOR
DesignatedPoint
+IAF
arcDirection = CWA (clockwise Arc)
fromAngle = 83
toAngle = 173
angleDirectionReference = TO
innerDistance = 15 NM
outerDistance = 25 NM
lowerLimit = 7100 ft
lowerLimitReference = MSL
CircleSector 1
arcDirection = CWA (clockwise Arc)
fromAngle = 83
toAngle = 173
angleDirectionReference = TO
innerDistance = 0 NM
outerDistance = 15 NM
lowerLimit = 5000 ft
lowerLimitReference = MSL
CircleSector 2
safeAreaType = LEFT_BASE
TerminalArrivalArea

## Slide 22: Miscellaneous - FAS datablock
The FAS data block is defined for RNAV GNSS approaches with LPV minima (SBAS)
guidanceSystem = LPV
FinalLeg
Note: The FAS DB can not be encoded as a whole (i.e. in one block) in AIXM 5.1 (E.g: AirportID)
Extracted from RTCA DO229-D

## Slide 23: Open questions
Procedure Designator
  SID, STAR -> which attribute should be used by default: designator or name ?
    Proposed answer: Designator
  InstrumentApproachProcedure: Define an attribute designator ?
    Proposed answer: Not necessary
How to encode the A424 recommended Navaid of a SegmentLeg ?
  Proposed answer: use TerminalSegmentPoint/PointReference/…

## Slide 24: Questions ?